Polyhedrons
Here is a football:
WE NEED A PICTURE OF A FOOTBALL

Flatten each face and we have a polyhedron.
WE NEED A DIAGRAM

Euler’s Formula:
F + V = E + 2 applies to any planar graph. It also applies to any polyhedron.
Here is a cube and we can represent it by a planar graph:

The cube has 8 vertices, the graph has 8 vertices. The cube has 12 edges, the graph has 12 edges.
The cube has 6 faces, the graph has 6 faces.
The face EFGH on the cube corresponds to the face EFGH on the planar graph. etc
The face ABCD on the cube corresponds to the outside face on the planar graph.
The cube and the planar graph have their vertices connected in the same way.
So the Euler formula must apply to the cube just as it applies to the planar graph.

Interior angles:
A cube has 6 faces. Each face has 4 interior angles. Each interior angle is 90°
So the sum of all the interior angles of a cube is 6times4 times 90°=2160°
Theorem
For any polyhedron
sum(interior angles)=(V-2)360°
Proof
See footnote 1

Let’s check this out for the cube:
V=8 so (V-2)360°=2160° as expected
Gaps:
Look at the football polyhedron. At each vertex, a regular pentagon and two regular hexagons meet.
If you put a regular pentagon and two regular hexagons together on a flat table then there is a gap:

Each interior angle of a regular pentagon is 108°
Each interior angle of a regular hexagon is 120°
So:
108°+120°+120°+gap=360°
So:
gap=12°
Descartes’ theorem
Take any polyhedron. Find the gap at each vertex. The sum of all these gaps will be 720°
Proof
see footnote 2
Example 1
A polyhedron has 3 regular pentagons meeting at each vertex. How many vertices are there?
108°+108°+108°+gap=360° so gap=36°
Now:
720over36=20 so this polyhedron has 20 vertices.
Example 2
A polyhedron has 2 regular pentagons and a square meeting at each vertex. How many vertices are there?
108°+108°+90°+gap=360° so gap=54°
Now:
720over54=13.3 so this polyhedron does not exist.

The regular polyhedrons.
Look at this cube:

This is a regular polyhedron because:
All the faces are identical.
All the faces are regular polygons.
All the vertices are surrounded by the same number of faces.
Theorem
There are only 5 regular polyhedrons
Proof
Consider a regular polyhedron where each face has n sides and r faces meet at each vertex.
Note:
n ≥ 3 and r ≥ 3 Can you see why?

If n = 3 and r = 3 then three triangles meet at each vertex.
60°+60°+60°+gap=360° so gap= 180° and 720over180 = 4 so we have 4 vertices

If n = 3 and r = 4 then four triangles meet at each vertex.
60°+60°+60°+ 60°+gap=360° so gap= 120° and 720over120 = 6 so we have 6 vertices

If n = 3 and r = 5 then five triangles meet at each vertex.
60°+60°+60°+ 60°+ 60°+gap=360° so gap= 60° and 720over60 = 12 so we have 12 vertices

If n = 4 and r = 3 then three squares meet at each vertex.
90°+90°+90°+gap=360° so gap= 90° and 720over90 = 8 so we have 8 vertices

If n = 5 and r = 3 then three pentagons meet at each vertex.
108°+108°+108°+gap=360° so gap= 36° and 720over36 = 20 so we have 20 vertices

If n = 3 and r ≥ 6 or n = 4 and r ≥ 4 or n = 5 and r ≥ 4 or n ≥ 6 and r ≥ 3
then you can easily check that the gaps are zero or negative and this is no good.
So there are only these 5 possibilities.
Example 3
Let’s check out the n = 5 and r = 3 polygon.
We know V = 20 What about E and F ?
Three faces meet at each vertex, so 3 edges meet at each vertex.
So E = 3V No!
Each edge is shared with 2 vertices.
So E = {3V} over2 = 30
But F + V = E + 2 so F = 12
This polyhedron is called a dodecahedron.

see Exercise 1

The semi-regular polyhedrons.
Look at the football polyhedron:
This is semi-regular polyhedron because:
All the pentagons are identical
All the hexagons are identical.
All the faces are regular polygons.
All the vertices are surrounded by the same set of faces in the same order.
Theorem
There are only 13 semi-regular polyhedrons.
We will not prove this and we will not try to find them all.
But let’s see if we can find some.
Example 4
Let’s check out the football polyhedron.
One pentagon and two hexagons meet at each vertex.
gap=12° and 720 over 12=60 So V=60 What about E and F ?
Three faces meet at each vertex. So 3 edges meet at each vertex.
So E = 3V No!
Each edge is shared with 2 vertices.
So E = {3V}over2 = 90
But F+V=E+2 So F = 32
We have 32 faces. P pentagons and H hexagons.
One pentagon meets at each vertex.
So P=V No!
Each pentagon joins five vertices.
So P=V over 5=12
Two hexagons meet at each vertex.
So H=2V No!
Each hexagon joins six vertices.
So H={2V} over 6=20
Check: T + H = F Good!

WARNING
We have been a bit sloppy.
SEE NOTES IN LEVER ARCH FILE

There are some polyhedrons, called prisms and anti-prisms, that seem to fit the description of a semi-regular polyhedron but are not included in the 13 semi-regular polyhedrons – check them out
see Exercise 2
see Exercise 3
EXERCISE 1
Check out the other 4 regular polyhedrons
EXERCISE 2
1) Can you find a semi-regular polyhedron where one triangle and two hexagons meet at each vertex?
2) Can you find a semi-regular polyhedron where one square and two pentagons meet at each vertex? CHANGE THIS – SAME AS EXAMPLE 2

EXERCISE 3
Use the pigeon-hole principle to show that you cannot have a polyhedron where every face has a different number of edges.
SOLUTIONS 1
tetrahedron	n=3 r=3 V=4 E={3V} over2=6 F=4
octahedron	n=3 r=4 V=6 E={4V} over2=12 F=8
icosahedron	n=3 r=5 V=12 E={5V}over2=30 F=20
cube	n=4 r=3 V=8 E={3V}over2=12 F=6
SOLUTIONS 2
1) gap= 60° and 720over60 = 12 So V = 12
Three faces meet at each vertex. So 3 edges meet at each vertex. So E = 3V No!
Each edge is shared with two vertices. So E = {3V}over2 = 18
But F+V=E+2 So F = 8
We have 8 faces. T triangles and H hexagons.
One triangle meets at each vertex. So T = V No!
Each triangle joins three vertices. So T = V over3 = 4
Two hexagons meet at each vertex. So H=2V No!
Each hexagon joins six vertices. So H={2V} over 6=4
Check: T+H=F Good!
2) gap= 54° and 720over54 = 13.33 So this is no good! CHANGE THIS – SAME AS EXAMPLE 2

SOLUTIONS 3
A polyhedron has 10 faces.
I have 7 boxes, labelled 3, 4, 5, 6, 7, 8, 9. I put each face in a box.
If a face has 7 edges then I put it in the box with 7 on the label. etc
There are 7 boxes and 10 faces. One (or more) box must contain two (or more) faces.
So two (or more) faces have the same number of edges.
note: each face has at least 3 edges
note: there are only 10 faces so a face cannot have 10 or more edges because each edge is connected to another face.
This proof will work however many faces the polyhedron has.

Footnote 1
Interior angles rule
Let’s find the sum of all the interior angles of any polyhedron.
The first face of our polyhedron has n sub1 sides.
The interior angles of this face add up to n sub1(180°)-360°	(remember?)
The second face of our polyhedron has n sub2 sides.
The interior angles of this face add up to n sub2(180°)-360°
etc
There are F faces
So:
sum(interior angles)=( n_{1}+ n_{2}+ n_{3}+...+n_{F})180°-F(360°)
Now:
E= n_{1}+ n_{2}+ n_{3}+...+n_{F} No!
Each edge is shared with two faces.
So:
E= {1} over {2} ( n_{1}+ n_{2}+ n_{3}+...+n_{F}) So n sub1+n sub2+n sub3+...+n_{F}=2E
So:
sum (interior angles)=2E(180° )-F(360°)=(E-F)360°
Now:
F+V=E+2 so E-F=V-2
So:
sum(interior angles)=(V-2)360°

Footnote 2
To find sum(interior angles) we looked at the faces of our polyhedron.
We looked at the faces of a cube and said:
A cube has 6 faces. Each face has 4 interior angles. Each interior angle is 90°
So the sum of all the interior angles of a cube is 6times4 times 90°=2160°
In general, we proved:
sum(interior angles)=(V-2)360°
by finding the sum of the interior angles of each face and then adding these up.

An alternative approach
We will look at the vertices of our polyhedron.
We look at the vertices of a cube and say:
A cube has 8 vertices. Each vertex is surrounded by 3 interior angles. Each interior angle is 90°
So the sum of all the interior angles of a cube is 8times 3 times 90°=2160°
We will use this approach to prove Descartes’ theorem.

At each vertex:
interior angles+gap=360°
So if we visit each vertex and add up all these angles:
sum(interior angles) + sum(gap) =sum 360°
Now:
sum(interior angles)=(V-2)360° and ∑ 360° = (V)360° so sum(gap)=720°